## Slide 1
POULAMI DAS
ECE, The University of Texas at Austin
QUANTUM COMPUTING SYSTEMS:
A SOFTWARE, ARCHITECTURE, and
Systems PERSPECTIVE -I
Why quantum computing? What topics will be covered? What are the requirements and expected outcomes?

## Slide 2
The Computing Stack- Why It Matters?
Full-stack Solutions are the key!
Application
Algorithm
Program
ISA
𝞵architecture
Circuits
Electrons
VS
Faster

## Slide 3
Abstractions & Transformations: Key To Computing
We will focus on the software, architecture, and systems aspect of quantum computing
Application
Algorithm
Program
ISA
𝞵architecture
Circuits
Electrons
Q Application
Q Algorithm
Q Program
Q ISA
Q Ctrl 𝞵arch
Q Circuits
Qubits
(atoms, ions)
Math, Quantum Information Theory
ECE/CSE
[Software, Architecture, & Systems]
Devices

## Slide 4
Quantum Bits (Qubits)
Quantum computers use qubits to encode information
Classical machines encode information using classical bits
  Either 0 or 1 at any given time (only two points on the sphere)
A qubit is the fundamental unit of information on a quantum computer
  Any combination of 0 and 1 at the same time (any point on the sphere)

## Slide 5
Superposition & Entanglement
Quantum computers use qubits to encode information
A qubit exists in a superposition of 0 and 1.
  A quantum system with ‘n’ qubits exist in superposition of all possible 2n states.
Entanglement enables us to create highly correlated states.
  This property allows us to efficiently manage the exponential state space.

## Slide 6
Quantum Gate Operations
H
X
Single-qubit gates
Two-qubit gates
H
X
Bit-flip/ NOT
Superposition
+
CNOT/ XOR
(Entanglement)
Bit-flip/NOT
Superposition
Quantum gates manipulate the state of qubits
Quantum gate operations rotate the qubits from one point to another

## Slide 7
Quantum Programs
Quantum programs manipulate qubits to amplify the probabilities of the correct output(s)
q0
q1
1
M
M
+
Chart: Initial state (q1q0)
| 00 | 01 | 10 | 11
 | 1 | 0 | 0 | 0
Chart: After H gate (q1q0)
| 00 | 01 | 10 | 11
 | 0.5 | 0.5 | 0 | 0
Chart: After CNOT gate (q1q0)
| 00 | 01 | 10 | 11
 | 0.5 | 0 | 0 | 0.5
2
3
4
3
2
1
Bell pair circuit
H
Bell-pair or Entanglement pair
H
H
T
T
OR
Quantum programs comprise of quantum operations

## Slide 8
Qubit Candidate Technologies
A (physical) qubit can be any two-level system that can exist in any quantum superposition of two independent (physically distinguishable) quantum states
Qubits are only a part of the quantum computing systems
Ion-trap qubits
Superconducting qubits
Quantum-Dot qubits
And others: Photonic qubits, topological qubits, neutral atom qubits
Notes: Trapped ions use ions as qubits and a trap that holds them in specific locations. They are controlled using a laser (or microwave)
and measured using photon detectors that detect the number of photons scatted during the readout operation.
Superconducting qubits are made up of Josephson junctions
that exhibit quantized energy levels when cooled to milli-Kelvin temperatures. Also known as artificial atoms, superconducting qubits are controlled using microwave signals.
Silicon spin/quantum dots are artificial atoms created by adding an electron to semiconductor materials (such as silicon atoms) and then the spin of the electron is controlled via microwave signals.

## Slide 9
Quantum Computer: Organization
Quantum computer = Qubits + Classical Control Processor + Software
Programs
Host
Software
Control
Processor
Qubit
Devices
Output
(Distribution)
Interface for access
Compilation
Output processing
Precise control to perform operations

## Slide 10
Key Challenge In Quantum Computing: Qubits Are Noisy
Quantum hardware errors lead to incorrect outputs during program execution
Chart: States/ Outcomes
| 00 | 01 | 10 | 11
 | 0.4 | 0.1 | 0.2 | 0.3
Qubit devices naturally lose their state even when left idle (decoherence)
Error
Imperfect quantum operations lead to computational errors
Correct (70%)
Erroneous (30%)
M
q0
q1
M
H
+
~ 10- 100 microseconds
Gate errors ~1 %
Measurement/Readout errors ~1-4 %
Classical bit error-rate ~10-18

## Slide 11
Quantum Error Correction (QEC)
QEC enables fault-tolerance but is expensive
Many noisy physical qubits
Fault-tolerant logical qubit
Logical error rate < physical error rate
50-1000 physical qubits
-> 1 logical qubit
QEC code

## Slide 12
Evaluating Qubit Device Technologies
Two vectors: Qubit lifetimes and operational fidelities + Scalability
It is too early now to bet on a single qubit device technology

## Slide 13
Available Quantum Systems + Future Roadmap
Objective is to scale up the systems while improving device error rates

## Slide 14
Noisy Intermediate Scale Quantum (NISQ)
NISQ systems run programs in the presence of errors
Near-term quantum computers with few hundreds of qubits: NISQ machines
2023
1,121 qubits
IBM
Condor
Typical system sizes
(up-to 433 qubits)
2025
4000+ qubits
IBM
Kookaburra
Too small for QEC
at application level
}
Preskill, “Quantum Computing in the NISQ Era and beyond”, 2018

## Slide 15
The Quantum Roadmap
Quantum computers must enable fault-tolerance in the long-run, NISQ-regime until then
Chart: Year
| 2017 | 2020 | 2023 | 2026 | Future
 | 5 | 16 | 27 | 65 | 127 | 433 | 1121 | 1386 | 4168 | 10000 | 20000 | 30000 | 40000 | 50000 | 100000 | 500000 | 1000000
Noisy Intermediate
Scale Quantum (NISQ)
Error
Mitigation
Fault Tolerant Quantum
Error
Correction

## Slide 16
NISQ Computing Model
Compile
Run
Log
Outcome
M
q0
q1
M
X
+
01
00
11
11
Program
Quantum
Device
Repeat N trials
Chart: States/ Outcomes
| 00 | 01 | 10 | 11
 | 25 | 25 | 0 | 50
11
Quantum
Executable
Can infer solution
Goal: Maximize probability of successful execution or trial (program success rate)

## Slide 17
Fault-Tolerant Quantum Computing
FTQCs extract information about errors and corrects them in real-time
QEC involves syndrome (parity) extraction and decoding to identify errors
Decoder
Control
Processor
Qubits
Readout
Interface
Syndrome
01…….01
Correction
QEC
Instructions
Did an error occur?
Where did the error occur?
What was the type of error?
1
1
Instructions to generate syndrome
2
2
Send syndrome to decoder
3
3
Send correction to control processor

## Slide 18
Key Role Of A Quantum Compiler
Controlled Gates: Bit-Flip versus Phase-Flip
creg c[2] ;
qreg q[2]; //qubit variable
H q[0]; //equal superposition
CNOT q[0], q[1]; //entangle
MEAS (q,c); //measure
Higher Quantum Assembly
Reset Q0
Reset Q1
z/4 pulse Qo
Set x/4 C0
z-z/2 pulse Qo, Q1
Meas pulse Q0
Meas pulse Q1
Lower Assembly
Time
Q0
Q1
S
1
1
//
//
//
//
Quantum
Compiler
Quantum_Func(2);
High Level Program
FPGA
S
Q0
Q1
Quantum compilers transform high-level programs into low-level sequence of control pulses

## Slide 19
NISQ Compilation Overview
Quantum compilers transform high-level programs into low-level sequence of control pulses
Circuit
Generator
Qubit
Mapper
Assembler/Nativizer
Executable
Quantum
Circuit
Mapped
Circuit
Quantum Compiler
Quantum
Program
Pulse
Scheduler
Nativized
Circuit

## Slide 20
From Quantum Program To Quantum Circuit
Controlled Gates: Bit-Flip versus Phase-Flip
Classical and Quantum operations are used
Circuit
Generator
Quantum Program
Unrolled sequence of quantum operations
Quantum Circuit
The quantum circuit is often represented as a DAG to capture the data dependencies

## Slide 21
From Quantum Circuit To Mapped Circuit
The scheduled and routed program is compatible with the topology of a device
q0
q3
q2
q1
Program
NISQ Device
SWAP
Scheduled/Routed Program
Qubit Allocation: Allocate each program qubit to a unique physical qubit
Qubit Routing: Introduce SWAPs to overcome limited device connectivity

## Slide 22
From Mapped Circuit To Nativized Circuit
The nativized circuit is compatible with the basis gate set of a specific device
Scheduled/Routed Program
H
RZ ()
RX ()
RZ ()
Gate Nativization
Gate Nativization: Translate each operation of the scheduled and routed program into a series of native gates that are specific to the device
Basis Gates/ Native Gates: The set of native gates supported by a device
Gate Nativization
RX()
RZ()
RX()
RZ()
RX()
q0
q1
XY
RX()
XY
q0
q1
+
CNOT

## Slide 23
From Nativized Circuit To Pulse Schedule
The pulse schedule is loaded onto FPGAs and used to generate the required waveforms
Pulse Scheduling: Translate each native operation into its equivalent pulse schedule

## Slide 24
NISQ COMPUTING
Why quantum computing? What topics will be covered? What are the requirements and expected outcomes?

## Slide 25
Where is the ACM India Quantum Summer School 2025 happening?
A. Solan
B. Kolkata
C. Bangalore
D. Delhi
A. Solan
20%
20%
20%
20%
A
B
C
D
40%
20%
20%
20%
A
B
C
D

## Slide 26
NISQ Objective: Maximize Program Success Rate
Software compiler optimizations are crucial to improve the success-rate of NISQ applications
Unroll loops/ Decompose multi-qubit operations
Cancel
Gates
Map
Qubits
Schedule + Route
Nativize
Gates
Cancel
Gates
Program
Generate Pulse Schedule
Run
Post-process
Use minimum gates
Use commutative properties, re-order operations
Efficient mapping to reduce SWAPs
Reduce SWAPs, select better-than-worst SWAPs
Another round of cancellations+ reordering
Optimize at pulse-level to reduce program length
Characterization Circuits OR Functionally identical copies
Correct Readout Errors
Cut and Stitch
Optimal native gate decomposition

## Slide 27
Qubit MaPPING AND ROUTING
Why quantum computing? What topics will be covered? What are the requirements and expected outcomes?

## Slide 28
Why Is Device Connectivity Limited?
Device connectivity depends on the qubit topology
Connectivity: Requires ‘connecting’ two qubits using resonators
Real devices have limited connectivity
Chart: # Qubits
| 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
 | 9900 | 39800 | 89700 | 159600 | 249500 | 359400 | 489300 | 639200 | 809100 | 999000
Impractical
IBMQ-Tokyo
Google Sycamore
IBMQ-Toronto
Rigetti Aspen

## Slide 29
Qubit Routing
SWAPs increase the overall gate count and depth of programs thereby, reducing fidelity
Key Objective: Minimize #SWAPs required to relocate a qubit from one point to another
SWAP Overheads: Increase in total number of two-qubit operations and circuit depth
Chart: QAOA Program Size (# Qubits)
| 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
Original | 12 | 20 | 30 | 42 | 56 | 72 | 90 | 110 | 132 | 156 | 182 | 210 | 240 | 272 | 306
Sycamore | 18 | 29 | 48 | 69 | 98 | 126 | 165 | 200 | 252 | 267 | 347 | 405 | 474 | 542 | 651
Toronto | 21 | 41 | 54 | 87 | 119 | 150 | 204 | 242 | 339 | 390 | 464 | 561 | 711 | 758 | 951
2x
3x
Google Sycamore
Max-Cut beyond 17 qubits

## Slide 30
Minimizing SWAPs As A Token Swapping Problem
Token swapping may be used to formulate the transformation of one qubit mapping to another
Given a graph G with nodes Vi and edges Eij
Each node has a token that can only be exchanged via SWAP with the neighbor
Token configuration f0 denotes the initial condition or arrangement of tokens
Find the minimum number of SWAPs to transform one token configuration f0 into another ft after swapping in t steps

## Slide 31
Implementation Example
SWAP minimization is NP-hard
Split program into independent layers
Transform (if required) the qubit mapping of ith layer into (i+1)th layer using SWAPs
cnot A,B
cnot C,D
cnot A,C
cnot A,D
L1
L2
L3
A
B
C
D
L1
L2
L3
S12
S23
B
D
C
A
Initial Qubit Allocation
C
A

## Slide 32
Multiple SWAP Candidates
A* search is not scalable
cnot A,B
cnot C,D
cnot A,C
cnot A,D
L1
L2
L3
B
D
C
A
C
A
SWAP A,C
B
D
C
A
B
A
SWAP A,B
B
D
C
A
C
D
SWAP C,D
B
D
C
A
B
D
SWAP B,D
A* search to locate candidates
Search complexity scales rapidly
Large memory footprint to store the A* search tree

## Slide 33
Lookahead Scheme
How far should you lookahead? What are the trade-offs?
cnot A,B
cnot C,D
cnot A,C
cnot A,D
cnot A,B
L1
L2
L3
B
D
C
A
C
A
B
D
C
A
B
A
B
D
C
A
C
D
B
D
C
A
B
D
SWAP A,C
SWAP A,B
SWAP C,D
SWAP B,D
SWAP insertion updates qubit mapping that impacts future operation scheduling
Choose the third SWAP candidate over the first one (CNOTs in layer L4 does not require any additional SWAPs in that case)
L4

## Slide 34
Quantum Then vs. Now: A Systems Approach
The constraints faced by the quantum software stack has evolved significantly in recent years
Quantum in 2016
Quantum in 2025
How to program a 5-qubit quantum computer?
What does a basic quantum API look like?
How can software mask hardware errors?
What do we need to run a quantum application?
How to manage classical - quantum interactions?
How to manage hardware errors at scale?
What do we need to support QEC?

## Slide 35
What’s The Central Theme Of The Systems Approach?
Hardware scaling (error rates and #qubits) must be accompanied with software scaling
Quantum in 2025
What do we need to run a quantum application?
How to manage classical - quantum interactions?
How to manage hardware errors at scale?
What do we need to support QEC?
Program 100-1000s of qubits
Manage multiple quantum, classical systems
Suppress/ mitigate errors on many qubits
Transition to many logical qubits
Scalability

## Slide 36
Quantum Cloud Services: Key Metrics Of Success
Quantum cloud services must optimize across multiple vectors
No to maximum control
Maximize profit
Lower resource management overheads (e.g. reduced downtimes for calibrations)
Minimum cost
Quality of solutions
Reduced wait times
Maximize resource utilization
Improve QoS
Manage diverse systems
Own vs. Third-party machines
Good classical support for apps

## Slide 37
Unified Software Stack For Diverse Quantum Eco-System
Key: Modularity
Runtime support for seamless access
Device + application specific compilation
Support for distributed computing
Support for QEC codes
Diverse users
Diverse applications
Diverse systems

## Slide 38
Device + Application Specific Optimizations
Exposing hardware and application characteristics improve the performance of compilers
Solve an optimization problem
Write program in high-level language
Translate to low-level gates to control qubits
Qubits use quantum mechanical properties
Map to quantum algorithm
Natural
language
Quantum
Software
Quantum
Hardware
Compiler
Noise-aware compilation, Tannu et al., Murali et al., ASPLOS’19
JigSaw, Das et al., MICRO’21
FrozenQubits, Ayanzadeh et al., ASPLOS’22
Elivagar, Anagolum et al., ASPLOS’23
Varsaw, Dangwal et al., ASPLOS’23
(JigSaw for VQEs)
Pulse scheduling, xtalk mitigation

## Slide 39
Even More Fine-grained Optimizations
Unsupervised learning assists in capturing fine-grained error characteristics
Strategies that work for one qubit may be insufficient at application level
  Applying dynamical decoupling (DD) to all idle qubits at application-level is sub-optimal
Complex for fine-grained learning
Simpler for fine-grained learning
ADAPT, Das et al., MICRO’21
  Only apply DD to qubits that benefit
Imitation Game, Das et al., HPCA’22
  What native gate to choose for translating high-level CNOTs?
OPTRAN, CAFQA, etc.
  Selecting optimal subset of compiler passes, assisting VQE

## Slide 40
Trade-offs Exist
Quantum software solutions must appropriately navigate different trade-offs
MIDAS, Das et al., MICRO SRC’22
  Improved heuristics for SWAP insertion
Performance
Complexity
Solvers
Heuristics
IDEAL
Compiler
Other areas?
FrozenQubits, Ayanzadeh et al., ASPLOS’23
  Application-aware cuts for QAOA
Performance
Complexity
Circuit cutting
Circuit
IDEAL

## Slide 41
Support For Distributed Computing
The goal is to parallelize and distribute the workload for end-to-end performance improvements
Different QPUs
(error rates, qubit types, sizes)
…
…
Different classical resources
(FPGAs, HPC clusters, GPUs)
Which QPU(s) should we use?
How to minimize overheads?
  Compilation
  Post-processing
  Training

## Slide 42
Support For Quantum Error Correction
Quantum software solutions must also support QEC in the near-term and beyond
QEC needs substantial software support
  High-level programmability, scheduling 1000s of operations per cycle, efficient resource management (cloud operations)
  Re-use existing software solutions as much as possible → improved programmers’ productivity, ease of software development
ERASER, Vittal et al., MICRO’23
  Speculative and adaptive insertion of leakage reduction circuits

## Slide 43
Final Thoughts About Quantum Software
Diversity
Modularity
Trade-offs
Full-stack approach