## Slide 1
POULAMI DAS
ECE, The University of Texas at Austin
QUANTUM COMPUTING SYSTEMS:
A SOFTWARE, ARCHITECTURE, and
Systems PERSPECTIVE -II
Why quantum computing? What topics will be covered? What are the requirements and expected outcomes?

## Slide 2
Applications To Devices Gap
Most practical quantum applications require error-rates far below device error-rates
2023
2026
203X
~400 qubits
p = 0.5%
~4000 qubits
p = 0.1%
~100K qubits
p = 0.01%
Goal
Applications-at-scale
p < 10-15
Significant gap in error rates!

## Slide 3
Quantum Error Correction- 101
What about phase errors?
Data qubits store information in entangled state, parity qubits detect errors
C
B
A
No error  Parity is all-zeros
0
0
0
1
One error  Parity is non-zero
(Hamming Weight 1)
1
1
1
One error  Parity is non-zero
(Hamming Weight 2)
1
1
0
1
0
One error  Parity is non-zero
(Hamming Weight 1)
Syndrome Extraction
Decoding
Syndrome
One bit-flip error

## Slide 4
Surface Codes
Logical error-rate decreases exponentially with increasing redundancy
Surface codes are widely recognized as the most promising QEC candidate
Correct more errors with increasing redundancy
(distance)
Logical Qubit

## Slide 5
Overview Of Quantum Error Correction Steps
Errors are actively corrected before they can accumulate
QEC involves syndrome (parity) extraction and decoding to identify errors
Decoder
Control
Processor
Qubits
Readout
Interface
Syndrome
01…….01
Correction
QEC
Instructions
Did an error occur?
Where did the error occur?
What was the type of error?
1
1
Instructions to generate syndrome
2
2
Send syndrome to decoder
3
3
Send correction to control processor

## Slide 6
QEC: Redundancy Buys Fault Tolerance
QEC is a complex game of probabilities
Pick a redundancy that meets application-level fault tolerance requirements
Error rate depends on number of operations
Error rate depends on physical qubit properties
QEC code, control, and decoder performance

## Slide 7
Quantum Error Correction Using Surface Codes
The distance is determined from the gap between the target (application) and device error-rate
More redundancy enables us to tolerate more errors (longer chains of errors)
Data qubits
Z stabilizers
X stabilizers
X Error
Z Error
}
Y Error
Regular
Surface Code
Rotated
Surface Code
Distance = 3
Distance = 3
Distance = 5
Logical Qubit

## Slide 8
How To Decode Errors?
There are other approaches to decode errors as well
Decoding can be translated into a graph matching problem
Code
Lattice
Decoding Graph
Z-Decoding Graph
X-Decoding Graph

## Slide 9
Overview Of Decoding Approaches
The MWPM algorithm is widely regarded as the gold-standard for decoding surface codes
Maximum Likelihood
Machine
Learning
Lookup
Table
Belief Propagation
Minimum Weight Perfect Matching
Union-Find
Graph Pairing
Others

## Slide 10
Overview Of QEC Process
Decoders must identify errors accurately or they may introduce errors themselves
Logical
Qubit
X
Z
Z
Syndrome Extraction
Decoder
X Syndrome: 0000
Z Syndrome: 1010
Correction
1
1
0

## Slide 11
Syndrome Extraction Is Imperfect
How do we handle errors in syndrome extraction?
Accuracy
Overheads
P
D
D
D
D
M
X
0
1
X
X
Handle errors in syndrome extraction
1
2
Handle complex patterns of errors

## Slide 12
Decode Multiple Syndromes Simultaneously
Decoders decode ‘d’ consecutive syndromes to tolerate errors during syndrome extraction
Errors that occur on (1) data qubits and (2) during syndrome extraction
Errors on data qubits: space
Measurement errors in syndrome extraction: time
Gate errors in syndrome extraction: space-time
Decoding-> Matching on a 3D graph with O(d) rounds
P
D
D
D
M

## Slide 13
Real-Time Decoding
Real-time decoding prevent the accumulation of errors and protects logical qubits
Real-Time Decoder
~1μs
Decoding must be in real-time to prevent the accumulation of errors
Required latency depends on the qubit technology
At least equal to the time to extract a syndrome

## Slide 14
Minimum Weight Perfect Matching (MWPM)
Ideally, we want to identify the MWPM in real-time
Edges: Data qubits
Nodes: Parity qubits
1s ->failed parity checks
Fully connected graph
Edge weight-> probability that the two nodes connecting the edge flips
Solve for MWPM
MWPM: denotes the highest probability error event

## Slide 15
Challenge: Software Decoders Are Too Slow
Software decoders are too slow for real-time decoding
Real-time decoding (within a microsecond) prevents accumulation of errors
Decoder
Control
Processor
Qubits
Readout
Interface
Syndrome
Correction
QEC
Instructions
Software
Decoder
15-20 mK
(Inside dilution refrigerator)
Room temperature
(Outside dilution refrigerator)
Traditionally, software decoders are used for decoding
Slow

## Slide 16
Limitations Of Software Decoding
Real-time decoders are crucial for QEC
Chart: Year
| 2011 | 2011 | 2011 | 2012 | 2014 | 2014 | 2015 | 2016 | 2018 | 2020 | 2020 | 2022
Repetition | 3 | 3 | 3 | 3 | 9 | 4 | 5 | 4 | 15 | 43 | 21 | 49
Surface | 4 | 7 | 17 | 17 | 7 | 19 | 24 | 49
Others | 5 | 7 | 4 | 1 | 5 | 5 | 3 | 5 | 1 | 3 | 15 | 11 | 1 | 10 | 7 | 23
Distance 5 Surface Code
Google, 2023
Distance 3 Surface Code
Wallraff Group, 2022

## Slide 17
REAL-TIME Decoding OF SURFACE codes
How can we decode surface codes in <1 us and achieve MWPM accuracy using hardware solutions?

## Slide 18
Use Lookup Tables Preloaded With MWPM
LILLIPUT: A low-cost, accurate, and real-time decoder for practical adoption
Control
Processor
Qubits
Readout
Interface
Syndrome
Correction
QEC
Instructions
Software
Decoder
Lookup Tables
Low-Cost
Low-Latency
Accurate
FPGA-based
Replace software decoders with LUTs
Poulami Das et al. “LILLIPUT: A Lightweight Low-Latency Lookup-Table Based Decoder for Near-term Quantum Error Correction”, ASPLOS 2022

## Slide 19
Programming LUTs Of LILLIPUT
LILLIPUT programs the LUTs offline using MWPM and performs decoding online
Program LUTs offline using software Minimum Weight Perfect Matching decoder
Control
Processor
Qubits
Readout
Interface
Syndrome
Correction
QEC
Instructions
Lookup Tables
Software
MWPM
000…000
000…001
111…111
…
00100000100
00000000000
LUT Data
All Error Events
…
00000100100
Offline Access
Preload LUT Data
Online

## Slide 20
Challenge: Memory Complexity Of LILLIPUT
LUT sizes exceed FPGA on-chip memory
28
[d=3]
[d=4]
[d=5]
224
216
148 MB
832 B
238 KB
Syndrome
Correction
Lookup Tables
LUT size grows exponentially with the number of syndrome bits
8-bit
16-bit
24-bit
28 = 256 entries
216 = 65K entries
224 = 16.7 Million entries
LUT size
Code distance

## Slide 21
Not All Error Events Are Equally Likely
Storing only entries for correctable errors are sufficient
Distance Surface Code = 3
Physical error rate = 0.1%
Rare
Uncorrectable
Logical error rate
Only store entries corresponding to correctable errors
0
0
No error (HW=0)
0
1
One error (HW=1)
1
1
One error (HW=2)
1
1
One error (HW=1)
An error flips at most two parity bits of each type

## Slide 22
LUTs Store Sparse Data
Compressed LUTs (CLUTs) store selective entries in compressed form
Can correct error chains
of length 1 only
Possible to assign errors
to only few data qubits at a time
Compress the LUT data

## Slide 23
Performance Of LILLIPUT
LILLIPUT decodes d=3 and limited form of d=5 in real-time
42 ns latency, < 7% FPGA logic,
Sufficient up-to d=5
CLUTs have negligible impact on accuracy
Up-to 107x memory reduction with CLUTs

## Slide 24
Rethinking MWPM And Matchings For Higher Distances
Goal: Locate this highest probability error event or the corresponding matching
a
b
d
c
W = -log(P(errors between c and d))
Pair bits such that sum of edge weights is minimized.
a
b
d
c
MWPM
Nonzero Syndrome Bits
Probability
Matchings = O(n!)
Lower weight

## Slide 25
Exhaustive Search For MWPM?
Insight 1: Low HW syndromes are easy to decode accurately
The number of perfect matchings scales O(eHW).
Look at small HW.
a
b
Only one option
c
d
e
f
Three options
i
j
k
x
y
z
= 15 options
5
* 3
* 1
Easy for exhaustive search

## Slide 26
Hamming weight (p = 10-4) | d = 3 prob. | d = 5 prob. | d = 7 prob.
0 to 2 (trivial) | 0.99 | 0.99 | 0.99
3 to 10 (low) | 4.2e-5 | 3.2e-5 | 0.01
>10 (high) | 0 | 0 | 4e-9
Logical error rate (LER) | 8.1e-6 | 1.3e-7 | 6e-9
Decreases exponentially
Only need to decode HW ≤ 10
Just exhaustively search for MWPM!
Matching Problem From Perspective Of Hamming Space
We only need to decode syndromes whose HW 10
P(HW > 10) < LER
Notes: We approach the problem of syndrome extraction through the perspective of Hamming weight.
First, we observe that for an error rate of 10^-4, syndromes with HW <= 10 comprise
all or almost all of the syndromes encountered during syndrome extraction.
We further observe that lower Hamming weights occur exponentially less often than higher Hamming weights.
Second, we observe that up to HW = 10, there are at most 945 possible perfect matchings. This low number, combined with the fact
That we need not decode HW > 10 implies that we can exhaustively search for the MWPM.
We leverage this fact to design Astrea to decode up to d=7.

## Slide 27
Decoding HW 6 And Below With Astrea
Astrea can quickly decode syndromes with HW ≤ 6 in 32ns
d
a
b
c
y
x
HW ≤6 = ≤32ns
MWPM
Suhas Vittal et al. “Astrea: Accurate Quantum Error-Decoding via Practical Minimum-Weight Perfect-Matching”, ISCA 2023

## Slide 28
Decoding HW 8 With Astrea
Astrea pre-matches a pair of bits and uses the HW-6 decoder 7 times to decode HW 8
d
a
b
c
x
y
HW ≤6 = ≤32ns
z
w
PM1
PM2
PM3
PM4
PM5
PM6
PM7
MWPM
min
HW 8 = 60ns
HW 8 Decoder

## Slide 29
Decoding HW 10 With Astrea
Astrea accurately decodes d = 7 in real-time with only 10% of the FPGA
HW ≤6 = ≤32ns
HW 8 = 60ns
HW 8 Decoder
e
a
b
c
d
x
y
z
u
v
HW 10 = 456ns
PM1
PM9
........
MWPM
HW 8 Decoder

## Slide 30
Coping With Larger Hamming Weights
Filter out large weights to reduce search space
a
Hamming weight = 16
~2M possible matchings!
Perror = 10-weight
Filter!
< LER
~2000 matchings
Notes: Currently,
*Astrea can handle d=7, p = 1e-4. If the physical error rate decreases,
then Astrea can handle higher distances. If the physical error rate increases,
Then Astrea cannot handle higher distances. This is because
Higher Hamming weights tend to appear more often at higher error rates and higher distances. Astrea cannot handle HW > 10, limiting its usability.
Thus, we want to extend Astrea to handle both higher distances and higher physical error rates.

## Slide 31
Finding MWPM Post Filtering
Prioritize lowest weights first to quickly find MWPM
Bits left:
16
14
12
10
8
6
Pre-matching
+
HW 6 MWPM
0
PM
MWPM

## Slide 32
Astrea-G :Design Overview
Astrea-G is the first decoder to accurately decode d = 9 in real-time
Filter out if w > WTH
15
8
4
2 | 15 | 4 | 6
15 | 8 | 14 | 8
4 | 14 | 13 | 15
6 | 8 | 15 | 12
Greedy
Pre-match
+
Global Weight Table
MWPM Register
HW ≤ 6?
t = 1μs
STOP!
Minimum
40% FPGA Utilization

## Slide 33
Performance Compared To MWPM
Astrea-G has comparable accuracy to MWPM, within 2.5x of its LER
Equal accuracy to MWPM for d = 7
Within 2.5x of MWPM for d = 9

## Slide 34
Astrea-G Under Tighter Constraints
Astrea-G works fine even below 1us
Extra time for:

## Slide 35
Summary
Hardware decoders are becoming more common in QEC
Surface codes
Real-time decoding
Lookup
Table
MWPM for d=3, limited d=5
MWPM up to d=9

## Slide 36
Future?

## Slide 37
QEC @ Scale: Need System-Level Thinking
How do we design the control processors? How do we transmit information?
Decoder
Control
Processor
Large Distances, 100s-1000s of Logical Qubits
Readout
Interface
Correction
QEC
Instructions
Syndrome
15-20 mK
(Inside dilution refrigerator)
Room temperature
(Outside dilution refrigerator)
4 K
(Inside dilution refrigerator)
4 K
Existing decoders do not account for the system-level constraints
Large bandwidth
More noise
Number of wires
100s Gbps
Inefficient

## Slide 38
Quantum Error Correction: Unique Challenges
Significant amount of research effort in QEC
Huge redundancy
Must be very fast
Imperfect process
System-level challenges
High overheads
(operations, qubits)
Operations at scale
Low coherence
Errors quickly accumulate
Both instruction delivery and decoding
Incorrect parities
Complex errors
(correlated, leakage)
Bandwidth
Cryogenic
Latency
Low overhead codes
Faster decoders (approx. algo., hardware)
Handling via decoding, scheduling
uarchitecture, compression, multi-level design